## Slide 1: OSI Model

## Slide 2: OSI Model
The Open Systems Interconnection (OSI) Reference Model is a conceptual framework that describes functions of the networking or telecommunication system independently from the underlying technology infrastructure.

## Slide 3: Seven layers
7 - Application
6 -Presentation
5 - Session
4 -Transport
3 - Network
2 - Data Link
1 - Physical

## Slide 4: 7 - Application
End User Layer
concerns the networking processes at the application level. This layer interacts directly with end-users to provide support for email, network data sharing, file transfers, and directory services, among other distributed information services.
Functions:
Access to network services
Examples: HTTP, FTP, POP3,WebSocket

## Slide 5: 6 - Presentation
Syntax Layer
converts data formats between applications and the networks.
Functions:
data conversion, character code translation, data compression, encryption and decryption
Examples: ASCII, EBCDIC

## Slide 6: 5 - Session
Synch & send to port
manages sessions between servers to coordinate the communication – as the first of the top three OSI model layers that deal with the software level. Session refers to any interactive data exchange between two entities within a network.
Functions:
opening, closing, and re-establishing session activities, authentication and authorization of communication between specific apps and servers, identifying full-duplex or half-duplex operations, and synchronizing data streams.
Examples:
API’s, Sockets, WinSock

## Slide 7: 4 - Transport
End-to-End Connections
ensures complete and reliable delivery of data packets. The Transport Layer provides mechanisms such as error control, flow control, and congestion control to keep track of the data packets, check for errors and duplication, and resend the information that fails delivery.
Functions:
Direct communication between end points and reliability
Examples: TCP, UDP, SCTP

## Slide 8: 3 - Network
Packets
organizes and transmits data between multiple networks. This layer is responsible for routing the data via the best physical path based on a range of factors including network characteristics, best available path, traffic controls, congestion of data packets, and priority of service, among others.
Functions:
implements logical addressing for data packets
Examples: IPv4, IPv6, IPsec, AppleTalk

## Slide 9: 2 - Data link
Frames
concerns data transmission between the nodes within a network and manages the connections between physically connected devices such as switches.
Functions:
The raw data received from the physical layer is synchronized and packaged into data frames that contain the necessary protocols to route information between appropriate nodes.
Examples: PPP, IEEE 802.22, Ethernet, DSL, ARP

## Slide 10: 1 - Physical
Physical structure
concerned with data communication in the form of electrical, optic, or electromagnetic signals physically transmitting information between networking devices and infrastructure.
Functions:
data Transmission Performance e.g. Bit Rate and Bit Synchronization; as well as modulation, switching, and interfacing with the physical transmission medium as described
Examples: USB